## Slide 1
Sensors
Training Presentation

## Slide 2: Topics
Introduction to sensors
Features
Interfacing
Pin Configuration
Types of sensors

## Slide 3
Introduction to Sensors

## Slide 4: What is Sensor ?
Introduction
Example
A sensor is a device that measures a physical quantity and converts it into a signal which can be read by an observer or by an instrument.
Sensors are used in everyday objects such as touch-sensitive elevator, buttons (tactile sensor) and lamps which dim or brighten by touching the base.

## Slide 5: Types of Sensors
Hardware
Sensors
Infrared Proximity Sensor
Sound Sensor
Temperature Sensor
Soil Moisture Sensor
Obstacle detector
Temperature& Humidity Sensor
Pressure Sensor

## Slide 6: Infrared Proximity Sensor
IR Sensor
Example
IR sensor works on the principle of emitting IR rays and receiving the reflected ray by a receiver (Photo Diode).
IR source (LED) is used in forward bias.
IR Receiver (Photodiode) is used in reverse bias.

## Slide 7: IR Sensor Circuit

## Slide 8: Voltage Comparator
LM358
LM358
A Comparator is a device which compares two voltages or currents and switches its output to indicate which is larger.
Comparator is also know as Op-amp.

## Slide 9: PIN Diagram LM358

## Slide 10: Sensor Interfacing with RPi

## Slide 11: Temperature Sensor LM35
Introduction
Example
The LM35 is an integrated circuit sensor that can be used to measure temperature with an electrical output proportional to the temperature (in oC).
The scale factor is 10mV/oC .

## Slide 12: Sensor Interfacing with RPi

## Slide 13: Sound Sensor
Introduction
Example
Sound Sensor is a simple microphone transducer based sensor based on the Transistor Amplification which converts from sound energy into electrical energy.
Adjustable range of detection.
Single bit active - high output.
3 - pin male header make it ready to use for breadboard

## Slide 14: 555 Timer IC
The 555 Timer IC is an integrated circuit (chip) implementing for variety of timer and multivibrator applications.
Introduction

## Slide 15: Pin Diagram
GND - Pin 1 connects the 555 timer chip to ground.
Trigger - The trigger is an active low trigger, which means that the timer starts when voltage on pin 2 drops to below 1/3 of the supply voltage.
Output - The output pin is where you would connect the load like led, motor etc.
Reset – Pin 4 is the reset pin. This can be used to reset the 555 timer’s timing operation.

## Slide 16: Pin Diagram
Ctrl Voltage - This pin is simply connected to GND, usually through a small capacitor, about 0.01 µF capacitor. It helps to level out any fluctuations in the power supply.
THR - The purpose of this pin is to monitor the voltage across the capacitor that's discharged by pin 7 .
DIS - This pin is used to discharge an external capacitor
Vcc – 4.5 V to 15 V

## Slide 17: Modes of Operation
Monostable Mode
Bistable Mode
Astable Mode

## Slide 18: Monostable Mode
In this mode, the 555 functions as a "one-shot"
Applications include timers, missing pulse detection, bouncefree switches, touch switches, frequency divider, capacitance measurement, pulse-width modulation (PWM) etc

## Slide 19: Monostable Mode
The pulse begins when the 555 timer receives a trigger signal.
The width of the pulse is determined by the time constant of an RC network, which consists of a capacitor (C1) and a resistor (R1).
The pulse width can be lengthened or shortened to the need of the specific application by adjusting the values of R and C.
T = 1.1 X R1 X C1

## Slide 20: Triggering Circuit of Sound Sensor

## Slide 21: Sound Sensor circuit

## Slide 22: Sensor Interfacing with RPi

## Slide 23: Soil Moisture Sensor
This soil moisture sensor is used to sense the present of water in soil and gives some output voltage to the processor to execute according to the instruction given by the user.
Introduction

## Slide 24: Feature of Soil Moisture Sensor
Power supply: 3.3v or 5v
Output voltage signal: 0~4.2v
Current: 35mA
Output – Analog & digital both
Feature

## Slide 25: Obstacle Detector HC-SR-04
This soil moisture sensor is used to sense the present of water in soil and gives some output voltage to the processor to execute according to the instruction given by the user.
Introduction

## Slide 26: Features of HC-SR-04
Power Supply :+5V DC
Working Current: 15mA
Measuring Angle: 30 degree
Ranging Distance : 2cm – 400 cm/1″ – 13ft
Trigger Input Pulse width: 10uS
Dimension: 45mm x 20mm x 15mm
Feature

## Slide 27: Pin Diagram of HC SR 04
VCC: +5VDC
Trig : Trigger (INPUT)
Echo: Echo (OUTPUT)
GND: GND
Pins

## Slide 28: Sensor Interfacing with RPi

## Slide 29: Temperature and Humidity Sensor DHT
DHT is a low cost Temperature and humidity sensor for electronic hobbyist, who wants to do data logging.
It has on board ADC chip for analog to digital conversion of data.
Introduction

## Slide 30: DHT 11
Ultra low cost
3 to 5V power and I/O
2.5mA max current use during conversion (while requesting data)
Good for 20-80% humidity readings with 5% accuracy
Good for 0-50°C temperature readings ±2°C accuracy
No more than 1 Hz sampling rate (once every second).
4 pins with 0.1" spacing
Features

## Slide 31: DHT 22
low cost
3 to 5V power and I/O
2.5mA max current use during conversion (while requesting data)
Good for 0-100% humidity readings with 2-5% accuracy
Good for -40 to 125°C temperature readings ±0.5°C accuracy
No more than 0.5 Hz sampling rate (once every 2 seconds)
4 pins with 0.1" spacing
Features

## Slide 32: Sensor Interfacing with RPi